Water Quality Testing & Monitoring

I. Temperature

- Temperature preferences vary between species

- Thermal stress and shock can occur when temperatures change more than 1-2 degrees in 24 hrs

II. Turbidity/Cloudiness

- High turbidity levels may damage gills and interfere with food gathering by fish

- Depth at which you can no longer see through the water is called the secci depth

- When the secci depth is more than 1 meter, submerged aquatic vegetation can survive easily

III. pH

- A range of 6.5 to 8.2 is optimal for most organisms

- Extreme acid and extreme alkaline conditions are hazardous

IV. Dissolved Oxygen (DO)

- A dissolved oxygen level below 3 ppm is stressful to most aquatic organisms

- DO of 8-9 is very good, below 4 is gravely polluted

V. Nitrate/Nitrogen

- Levels above 10 ppm considered unsafe for drinking water

- Unpolluted water has level below 1 ppm

VI. Phosphate

- Total phosphorus levels higher than 0.03 ppm contribute to increased plant growth

- Levels above 0.1 ppm can cause plant growth beyond normal eutrophication

VII. Hardness

- Defined as the amount of calcium and magnesium (primarily), both of which enter the water mainly by leaching from rocks

- Hard water = high amounts of Ca and Mg

- Soft water = low amounts of Ca and Mg

VIII. Coliform Bacteria

- Permissible fecal coliform levels are lowest for drinking water/well water, a little higher for swimming, and the highest for boating and fishing

IX. Salinity

- Defined as the total of all salts dissolved in the water

- Seawater = 35 ppt (parts per thousand), freshwater = 0 ppt

X. Carbon Dioxide

- Above 25 ppm is harmful to most gill breathers

*Other tests include color, odor, biotic survey, etc.